SECTION 10 28 13.14

ELECTRIC HAND DRYERS

GENERAL

CONDITIONS AND REQUIREMENTS

The General Conditions, Supplementary Conditions, and Division 01 – General Requirements apply.

SECTION INCLUDES

Electric hand dryers.

RELATED SECTIONS

Specifier Note:  In this article, specify work specified in other sections that is related to work of this section.

Division 26 - Electrical:  Electrical systems and components.

Specifier Note:  The following paragraph is a sample that may be used in this article.  Add to or delete from the following as appropriate for the specific project.

Section [xxxxx] – [Section Title]:  [Include brief description of work specified in another section that is related to the work of this section.]

SUBMITTALS

Specifier Note:  In this article, specify various types of data to be furnished by the contractor before, during, or after construction. Topics included in this article are:  product data, shop drawings, samples, design data, test reports, certificates, manufacturers’ instructions, manufacturers’ field reports, qualification statements, and closeout submittals.

Submit under provisions of Section [01 33 00] [______].

Product Data:  Provide construction details, dimensions, anchoring and mounting requirements, material and finish descriptions, electrical requirements, and manufacturer's warranty.

Operation and Maintenance Data:  Provide for electric hand dryers to include in maintenance manuals.

Warranty:  Provide sample of manufacturer’s standard warranty for parts and labor.

QUALITY ASSURANCE

Specifier Note:  In this article, describe qualifications, regulatory requirements, certifications, field samples, mock-ups, and pre-installation meetings.

Product Certification:  ETL listed in accordance with UL 507.  National Sanitation Foundation (NSF) Protocol P335 "Hygienic Commercial Hand Dryers" compliant.

Electrical Components, Devices, and Accessories:  Listed and labeled in accordance with NFPA 70, by a qualified testing agency, and marked for intended location and application.

DELIVERY, STORAGE AND HANDLING

Deliver, store, and handle electric hand dryers in manufacturer's protective packaging.

Store electric hand dryers off of ground, under cover, and in a dry location.  Handle according to manufacturer's written recommendations to prevent damage, deterioration, or soiling.

COORDINATION

Coordinate locations of electric hand dryers with other work to prevent interference with clearances required for access, and for proper installation, adjustment, operation, cleaning, and servicing of electric hand dryers.

WARRANTY

Manufacturer's Standard Warranty:  Manufacturer's standard form in which manufacturer agrees to repair, restore, or replace defective electric hand dryer components and labor within specified warranty period.

Warranty Period:  Five (5) years limited for labor and five (5) years for parts.

PRODUCTS

MANUFACTURERS

Basis-of-Design Product:  Subject to compliance with requirements, provide the electric Dyson Airblade V  hand dryers manufactured by Dyson Inc., 600 W. Chicago Avenue, Suite 275, Chicago, IL 60654; 888-397-6622, http://wwwdyson.com/hand-dryers or comparable product acceptable to the Architect.

Substitutions will be considered under provisions of Section 01 25 00.

ELECTRIC HAND DRYERS

Specifier Note:  In the below paragraph, retain the first option if the high voltage white finish is specified; retain the second option if sprayed nickel high voltage finish is specified; retain the third option if the white low voltage finish is specified; or retain the fourth option if the sprayed nickel low voltage finish is specified.

Electric Hand Dryers:  The electric Dyson Airblade V Electric hand dryer (Model HU02); Item No. [307171-01 (white HV)] [307172-01 (sprayed nickel HV)] [307173-01 (white LV)] [307174-01 (sprayed nickel LV)].

Mounting:  Surface mounted on ABS/PBT plastic backplate/mounting bracket; protrudes four inches from wall, no recessing required; ADA compliant.

Specifier Note:  Retain the first option in the subparagraph below if the sprayed nickel finish is specified; retain the second option if the white finish is specified.

Construction:  Polycarbonate casing with anti-microbial [additive in paint] [molded additive].  Anti-microbially integrated external plastics and seals.  Anti-tamper M4 exterior pin-hex screws.  Water ingress protection to IP24.

Specifier Note:  For Point 3 in the subparagraph below, retain the first option below if the sprayed nickel finish is specified; retain the second option if the white finish is specified. For Point 7 in the subparagraph below, retain the first option if the low voltage is specified; retain the second option if the high voltage is specified.

Color Finish:  [Sprayed nickel] [White] finish.

Filtration:  99.97 percent particulate efficiency HEPA filter with anti-microbial coating.

Operation:  Touch-free capacitive sensor activation.

Hand dry time:  12 seconds

Airspeed at nozzle:  420 mph

Operating Airflow:  Up to 5.28 gal/sec.

Rated Operating Noise Power:  79 db(A)

Motor:  Dyson Digital Motor (DDM), V4 switched reluctance brushless DC type; 92,000 rpm motor speed; less than 0.5 watt standby power consumption.

Electrical Requirements:  [110-127 V AC, 12 A, 1000 W]  [200-240 V AC, 10 A, 1000 W] Dyson recommends 15 amp circuit.

Operating Temperature Range:  0 - 40 degrees C.

Standby Power Consumption:  Less than 0.5 W.

EXECUTION

EXAMINATION

Verify availability and characteristics of electrical power.  Drill minimum two (2) inch diameter holes for electrical service entrance through backplate.

Do not begin installation until substrates are complete and ready for installation of electric hand dryers.

INSTALLATION

Locate and install mounting bracket in accordance with manufacturer’s written instructions.  Use minimum 0.25-inch anchors to mount bracket.  Mount electric hand dryer at height above finished floor recommended by manufacturer.

Install electric hand dryer in accordance with manufacturer’s written instructions, using fasteners appropriate to substrate indicated and recommended by manufacturer.  Install electric hand dryers level, plumb, and firmly anchored in locations and at heights indicated.

CLEANING AND PROTECTION

Adjust electric hand dryers for smooth operation.  Replace damaged or defective components.

Remove protective coverings from finished surfaces.

Clean exposed surfaces using materials and methods recommended by manufacturer.

END OF SECTION

© 2017 Dyson Airblade™.  All Rights Reserved.

A copyright license to reproduce this specification is hereby granted

to non-manufacturing engineers, architects and specification writers.

New 04/13